## Slide 1
Mini Soccer
Penalty Kick Game
Tianpai Le, Yuehan She & Renkun Wang
AME-504, Mechatronics System Engineering
Application Development Project​
1

## Slide 2
Table of Contents
2
Context & Project Goal | 3
Projectile Launcher Design | 6
Field & Goalkeeper Design | 13
Electronics & Software Design | 14

## Slide 3
Context & Project Goal
Design a mini soccer game that imitates a penalty kick:
A projectile launcher shoots a ball towards the goal
Launcher can be controlled by player
A moving obstacle acting as the goalkeeper
3

## Slide 4
Context & Project Goal
Projectile Launcher: 3-DOF System
X-Translation
(adjustable force)
Y-Rotation
Z-Rotation
Moving Goalkeeper
Operated by remote control
4

## Slide 5
Projectile Launcher: X-Translation Design
Linear Screw
Compression Spring
Front Slider
Nut & Rear Slider
N20 DC Motor
Sliding Rail
Trigger
5

## Slide 6
Elastic Potential Energy:
Conversion to Ball Kinetic Energy:
Ball Instantaneous Positions:
-- Spring Rate
-- Maximum Load
-- Efficiency (assume 25%)
-- Initial Projectile Velocity
-- Projectile Angle
Spring Equations
Projectile Launcher: X-Translation Design
6

## Slide 7
Available rubber ball diameters:
0.43’’
0.5’’
0.68’’
MATLAB Calculator: Projectile Motion
Projectile Launcher: X-Translation Design
7

## Slide 8
No. | Spring Name | Neutral Length | Outside Diameter | Max Load [lb] | Spring Rate [lb/in] | Adjustable Length | Rubber Ball Diameter | Max Distance @ 30° [in]
1 | 9657K228 | 3.5'' | 0.375'' | 2.87 | 2.87 | 1'' | 0.43'' | 350-400
2 | 9657K226 | 3.5'' | 0.438'' | 4.77 | 3.25 | 1.47'' | 0.43'' | 900-1000
3 | 9657K115 | 3'' | 0.5'' | 6.15 | 3.77 | 1.63'' | 0.5'' | 800-900
4 | 9657K221 | 4.5'' | 0.563'' | 11.15 | 5.16 | 2.16'' | 0.5'' | 1600-1800
5 | 9657K126 | 3'' | 0.593‘’ | 7.49 | 4.59 | 1.631‘’ | 0.5'' | 1000-1100
6 | 9657K432 | 3'' | 0.6'' | 7.3 | 3.1 | 2.38'' | 0.68'' | 500-600
7 | 9657K449 | 3.5'' | 0.6'' | 7.3 | 2.7 | 2.79'' | 0.68'' | 600-700
8 | 9620K57 | 3'' | 0.656'' | 9.38 | 7 | 1.34'' | 0.68'' | 400-450
9 | 9657K124 | 3'' | 0.688'' | 3.56 | 1.9 | 1.871 | 0.68'' | 200-220
Source: McMaster-Carr
Criteria:
Longer adjustable length
Shorter shooting distance
Spring Selection
Projectile Launcher: X-Translation Design
8

## Slide 9
Projectile Launcher: Y-Rotation Design
9
Roller
Y-Rotation Board
Track

## Slide 10
Point B Coordinates:
Projectile Elevation Angle, β
-- Roller Radius
Geometric Equations for Linkages
Projectile Launcher: Y-Rotation Design
10

## Slide 11
MATLAB Calculator: Y-Rotation Mechanism Geometry
Projectile Launcher: Y-Rotation Design
11

## Slide 12
Projectile Launcher: Z-Rotation Design
Motor Position
Position of Structural Support for Stability
12

## Slide 13
Field & Goalkeeper Design
13
Goalkeeper
Field & Goal

## Slide 14
Electronics & Software Design
Schematic
Power
Ground
Digital
PWM
X-Translation Motor
Rotation Servos
IR Receiver
Remote Control
Arduino Board
14

## Slide 15
Start
Z-Rotation
Y-Rotation
X-Translation
Launch
Goal Sensor & Display
Electronics & Software Design
Logic Process
Power Button
Play/Pause Button
Timer
(stop automatically if button not pressed)
15

## Slide 16
Thank you for Listening!
Q&A
16